## Slide 1: KSPECDR Flux Calibration Pipeline
End-to-End Process Overview
  Project: kspecdr
  Goal: convert extracted counts to physical flux density (erg/cm2/s/A)
  Entry point: reduce_object(args)
  Flux calibration stage: _apply_fluxcal(red_filename, args)

## Slide 2: Where Flux Calibration Happens
Reduction Order in reduce_object
  Raw -> IM (make_im)
  IM -> EX (make_ex)
  EX -> RED copy
  Flat-field, scrunch, throughput correction, sky subtraction
  Flux calibration (CALIBFLUX=True)
  Final metadata + reduced status
Key point: flux calibration runs after wavelength calibration and sky subtraction.

## Slide 3: Inputs Required for Flux Calibration
Science Data + Metadata
  RED spectra + variance + wavelength solution (WAVELA)
  Fiber table with fiber types and names (FIBRES)
  Standard fibers identified by TYPE='C'
External Resources
  Standard-star photometry CSV (CALIBFLUX_CATALOG)
  BOSZ template library (data/templates/bosz2024/)
  Filter curves (data/filters/*.dat)
  Mask regions (data/masks/telluric_default.dat)

## Slide 4: Standard-Star Selection
Fiber and Catalog Mapping
  Pipeline scans fibers and keeps only calibration fibers (TYPE='C')
  For each selected fiber:
    Build observed Spectrum1D (wavelength, flux, variance, mask)
    Read star name from fiber table (if present)
    Load photometry row from catalog
Current implementation detail: - Catalog matching is by row index order (not RA/Dec positional matching yet).

## Slide 5: Template Matching (Per Standard Star)
Best-Fit Stellar Model Selection
  Estimate Teff search range from broadband colors
  Query BOSZ candidates in parameter box (Teff/logg/[M/H])
  For each candidate:
    Convolve to instrument resolution (CALIBFLUX_FWHM or SPECFWHM)
    Resample to observed wavelength grid
    Measure RV by log-lambda cross-correlation
    Continuum-normalize observed and template spectra
    Score fit (chi2 or huber)
  Select best template + RV

## Slide 6: Photometric Scaling
Set the Absolute Flux Level
  Compute synthetic photometry of the best template through loaded filters
  Compare to observed catalog magnitudes (internally converted to AB)
  Derive a weighted scale factor from magnitude offsets
Formula used: - scale = 10^(-0.4 * mean_delta_mag)
Output: - Scaled template spectrum in physical flux units - Scale uncertainty from photometric errors

## Slide 7: Per-Star Calibration Vector
Build Cal_star(lambda)
  Core relation:
    Cal_star(lambda) = F_model_scaled(lambda) / C_obs(lambda)
  Mask invalid pixels:
    non-finite values
    non-positive flux
    telluric/bad wavelength regions
Variance model: - Var(Cal) = Cal^2 * [Var(model)/model^2 + Var(obs)/obs^2]
Each star yields one CalibrationVector with metadata (Teff, logg, [M/H], RV, scale).

## Slide 8: Combine Multiple Standards
Robust Combined Calibration Curve
  Input: per-star calibration vectors
  Default method: inverse-variance weighted mean
  Iterative sigma clipping (default 3 sigma)
  Optional smoothing: Savitzky-Golay (CALIBFLUX_SMOOTH=True)
Special case: - If only one standard star is available, pass-through without combination.
QC metric: - RMS fractional scatter across stars vs wavelength

## Slide 9: Apply Calibration to All Fibers
Final Flux and Variance Update
For every fiber spectrum: - F_cal = Counts * Cal_combined - Var_cal = Var_counts * Cal^2 + Counts^2 * Var_calibration
Write back to RED file: - Calibrated science image - Propagated variance - Header keywords: BUNIT, FLUXCAL, FCALNSTR, FCALRMS - HISTORY lines per standard star (template parameters, RV, scale)

## Slide 10: Runtime Controls (args)
Main FluxCal Arguments
  CALIBFLUX (bool): enable flux calibration
  CALIBFLUX_CATALOG (str): standard-star catalog CSV path
  CALIBFLUX_FWHM (float): instrument FWHM in Angstrom
  CALIBFLUX_METRIC (chi2 or huber)
  CALIBFLUX_SMOOTH (bool): smooth combined curve
Recommended minimum: - set CALIBFLUX=True - provide CALIBFLUX_CATALOG - ensure fibers include at least one TYPE='C'

## Slide 11: Practical Example (Commissioning Data)
Example Resource Paths
  Assign file: resources/comm/assign/tile_058.assign.txt
  Standard-star catalog:
    resources/comm/20260129/calib/standard_star_atlas_refcat2.csv
Example fiber classes from assign table: - target_class=8 -> standard star -> TYPE='C' - target_class=9 -> sky fiber -> TYPE='S'

## Slide 12: QC Checklist
Validate Calibration Quality
  Confirm FLUXCAL=True in final RED header
  Check number of standards used (FCALNSTR)
  Inspect scatter (FCALRMS) and per-star HISTORY entries
  Plot combined and per-star vectors (fluxcal/qc.py utilities)
  Verify calibrated spectra units are erg/cm2/s/A

## Slide 13: Known Gaps and Next Improvements
Current Limitations
  Catalog-to-fiber matching is index-based; positional matching is TODO
  Calibration quality depends on available standard stars and photometric bands
  Telluric correction stage is separate and optional (TELCOR)
Planned Enhancements
  RA/Dec-based catalog association
  tighter QC gating and automated outlier rejection policies
  richer nightly transfer-function handling

## Slide 14: Summary
Flux Calibration in This Pipeline
  Uses in-field standard stars (TYPE='C')
  Fits BOSZ templates with RV + continuum normalization
  Anchors absolute scale with catalog photometry
  Combines per-star vectors robustly
  Applies calibrated flux conversion to every fiber with full variance propagation
Deliverable: physically calibrated RED spectra ready for science analysis.